## Slide 1: Introduction to Information Theory
Dr. Arup Kumar Pal
Department of Computer Science & Engineering
Indian Institute of Technology (ISM)
Dhanbad, Jharkhand-826004
E-mail: arupkrpal@iitism.ac.in

## Slide 2: Outline
Introduction
Digital communication System
Shannon Information
Entropy
Information Theory

## Slide 3: Introduction
A communication system is a system which sends information from one place to another.
Information Theory answer two fundamental questions in communication theory:
  What is the ultimate data compression?
  What is the ultimate transmission rate of communication?

## Slide 4: Contd…
Encoded data is considered during transmission due to three reasons:
  For compact representation ( Source Coding)
  For error detection/correction (Coding Theory)
  For secrecy/authentication (Cryptography)

## Slide 5: Communication System
General model of a communication system
Source
Channel
encoder
Encryption
Modulator
Source
encoder
Channel
Demodulator
Decryption
Channel
decoder
Source
decoder
Destination

## Slide 6: Source
The source is usually modeled as a random process.
It can be discrete or continuous in value and in time.
Two type of source are considered:
  Memory less Source: Each symbol independent of the previous one.
  Markov Model: Each symbol depends on the previous one.

## Slide 7: Source Coding
The goal of source coding for digital systems is two fold:
  Uniquely map any arbitrary source message to a binary code and back again.
  Efficiently map a source message to the most compact binary code and back again.
Techniques are
  Fixed-length code
  Variable-length code (Goal: Minimizing the average code word length)

## Slide 8: Source Coding
To send a message from a source to a destination, a symbol is normally coded into a sequence of binary digits.
The result is called code word
A code is a mapping from a set of symbols into a set of code words.
Example, ASCII code is a mapping of a set of 128 symbols into a set of 7-bit code words
    A -----------------------> 0100001
    B -----------------------> 0100010
    Set of symbols------> Set of binary streams

## Slide 9: Fixed- and Variable-Length Code
A code can be designed with all the code words the same length (fixed-length code) or with different lengths (variable length code)
  Examples
    A code with fixed-length code words:
      S1 -> 00; S2 -> 01; S3 -> 10; S4 -> 11
    A code with variable-length code words:
      S1 -> 0; S2 -> 10; S3 -> 11; S4 -> 110

## Slide 10: Example-1
Consider the following sequence BDBCACDBCDBDBDACDA
Total No of Characters: 18
Representation of Code:
00 for A, 01 for B, 10 for C and 11 for D
Here the sequence is generated by a process that follows the following rules: (i) A is followed by B or C; (ii) B is followed by C or D; (iii) C is followed by A or D; (iv) D is followed by A or B
B | D | B | C | A | C | D | B | C | D | B | D | B | D | A | C | D | A
01 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 0

## Slide 11: Channel Coding
Channel coding is considered for reliable communication between transmitter and receiver.
Two policies to deal with channel coding are:
  Forward Error Correction (FEC)
  Automatic Repeat Request (ARQ)

## Slide 12: Transmitting
Coding theory uses redundancy to transmit binary bits of information
0
coding
1

## Slide 13: Transmitting
Coding theory uses redundancy to transmit binary bits of information
0 000
coding
1 111
Transmission
010
110
Reconstruction
at reception
(correction)
000
111
errors
(2nd Principle)

## Slide 14: Information Theory
Shannon’s information theory deals with limits on data compression (source coding) and reliable data transmission (channel coding)
  How much data can be compressed?
  How fast can data be reliably transmitted over a noisy channel?
Two basic “point-to point” communication theorems(Shannon 1948)
  Source coding theorem: the minimum rate at which data can be compressed lossless is the entropy rate of source.
  Channel coding theorem: The maximum rate at which data can be reliable transmitted is the channel capacity of the channel.

## Slide 15: Measure of Information
The information content of a message is inversely proportional to the probability of the occurrence of that message.
If a message is very probable, it does not contain any information. If it is very improbable, it contains a lot of information

## Slide 16
Assume a memoryless source with
  alphabet A = (a1, …, an)
  symbol probabilities (p1, …, pn).
How much information do we get when finding out that the next symbol is ai?
According to Shannon the self information of ai is

## Slide 17: Self Information
The self information of I(ai) of an event ai depends soley on P(ai) based on the following assumption:
  I(ai) must be a decreasing function of P(ai): more an event is likely, the less information its occurrence brings to us.
  I(ai) =0 if P(ai) =1 since if we are certain (there is no doubt) that E will occur, we get no information from its outcome.
  I(ai) + I(bi) if A and B are independent.
The only function satisfying the above axioms is the logarithmic function:

## Slide 18
Assume two independent events A and B, with probabilities P(A) = pA and P(B) = pB.
For both the events to happen, the probability is pA . pB. However, the amount of information should be added, not multiplied.
No, we want the information to increase with decreasing probabilities, so let’s use the negative logarithm.
Logarithms satisfy this!

## Slide 19: Message Information
If the message comes from a Memory less source, each symbol is independent and the probability of receiving a message with symbols Si, Sj, Sk, … (where i, j, and k can be the same) is:
    P(message) = P(Si)P(Sj)P(Sk) …
Then the information content carried by the message is

## Slide 20: Units
log2 units are bits (from 'binary')
log3 units are trits(from 'trinary')
loge units are nats (from 'natural logarithm')
log10 units are Hartleys

## Slide 21: Information Theory
Shannon’s Information theory deals with:
  Limits on Data Compression-(Source Coding)
  Reliable Data Compression-(Channel Coding)

## Slide 22: Basic Communication Theorems
SOURCE CODING THEOREM
The minimum rate at which data can be compressed losslessly is the entropy rate of the source.
CHANNEL CODING THEOREM
The maximum rate at which data can be reliably transmitted is the channel capacity of the theorem.

## Slide 23: Source Coding Theorem
Establishes the limit to possible data compression
Provides lower and upper bound of data compression
where,
Entropy
Average Length

## Slide 24: Information Channel
CHANNEL: Medium to transmit some data
INFORMATION CHANNEL: Physical transmission medium over which information is transmitted from transmitter to receiver
CHANNEL REPRESENTATIONS:
Channel Matrix
Channel Diagram
Joint Probability Matrix

## Slide 25: Information Channel
CHANNEL MATRIX: Graphical representation of communication channel in the form of a matrix
y1 y2 … ym
x1 P(y1 / x1) P(y2 / x1) … P(ym/ x1)
x2 P(y1 / x2) P(y2 / x2) … P(ym/ x2)
:
xn P(y1 / xn) P(y2 / xn) … P(ym/ xn)

## Slide 26: Information Channel
y1 y2 y3
x1 P(y1 / x1) P(y2 / x1) P(y3/ x1)
x2 P(y1 / x2) P(y2 / x2) P(y3/ x2)
x3 P(y1 / x3) P(y2 / x3) P(y3/ x3)
x1
x2
x3
y1
y2
y3
Channel Matrix Channel Diagram
A discrete communication channel with 3 inputs & 3 outputs
P(y1 / x1)
P(y3/ x3)

## Slide 27: Channel Coding Theorem
A DMS producing H(X) in Ts sec
Information generated per sec = H(X) / Ts
Channel Capacity = C
Maximum of C information can be transmitted in Tc sec
Information transmission rate = C/ Tc
For reliable Channel Coding,
H(X) / Ts <= C/ Tc
Code Rate <= Critical Rate

## Slide 28: Conclusions
In this lectures, brief over of information theory is presented.
Several source coding mechanism will be discussed
In addition different error detection and correction techniques will be presented.

## Slide 29: Textbooks
Fundamentals of Information Theory and Coding Design by Roberto Togneri and C. J. S. deSilva.
Introduction to Error Control Codes by S. Gravano
Introduction to Data Compression by Khalid Sayood.
Information Theory and Coding by Muralidhar Kulkarni and K. S. Shivaprakasha