## Slide 1: Introduction to Cyclic Codes
Dr. Arup Kumar Pal
Department of Computer Science & Engineering
Indian Institute of Technology (ISM)
Dhanbad, Jharkhand-826004
E-mail: arupkrpal@iitism.ac.in

## Slide 2: Cyclic Codes
It is a subclass of Linear Block Codes
Definition:
  ie. If C= (Cn-1, Cn-2, …, C2, C1, C0) is a code vector,
  Then C’=(Cn-2, …, C2, C1, C0 ,Cn-1) is also a code vector
An (n,k) linear block code C is a cyclic code if every cyclic shift of a codeword in C is also a codeword in C

## Slide 3: Algebraic Description of Cyclic Code
Every cyclic codeword can be represented as a polynomial
For an (n,k) cyclic code,
Maximum degree of codeword=n-1
Polynomial representation of C=(cn-1, ..., c2,c1,c0) is :
c(x)= cn-1xn-1 +…+ c2x2 + c1x + c0

## Slide 4: Cyclic Codes
Non-systematic codeword
c(x) = i(x).g(x)
Systematic codeword
c(x) = xn-k . i(x) + R g(x) xn-k . i(x)
Steps to Find Systematic Codeword:
v(x) = xn-k . i(x)
r(x)= R g(x) xn-k . i(x)
c(x) = v(x) + r(x)
where, g(x) is Generator Polynomial
i(x) is Information Polynomial

## Slide 5: Generator Polynomial
Definition:
Maximum degree of g(x)= n-k
Polynomial Representation of g(x):
In an (n,k) cyclic code there exist a unique generator polynomial from which all the codewords can be generated
g(x) = gn-kxn-k + gn-k-1xn-k-1 +…+ g1x + g0

## Slide 6: Theorem 1
Proof:
Let g(x) and g’(x) be two non-zero code polynomial of minimum degree r=n-k
g(x) = xn-k + gn-k-1xn-k-1 +…+ g1x + 1
g’(x) = xn-k + g’n-k-1xn-k-1 +…+ g’1x + 1
C’(x) = g(x)+g’(x) (By linearity property)
=(gn-k-1+ g’n-k-1)xn-k-1 +…+ (g1+g’1)
C’(x) is a code polynomial of degree < n-k (Contradiction) Hence, g(x) is unique
Assume g(x) is not unique
The non-zero code polynomial of minimum degree in a cyclic code C is unique

## Slide 7: Theorem 2
Let g(x) = gn-k-1xn-k + gn-k-1xn-k-1 +…+ g1x + g0
be the nonzero code polynomial of minimum degree in an (n,k) cyclic code C.
Then,
Proof:
Assume g0=0
g(x) = xn-k + gn-k-1xn-k-1 +…+ g2x2 + g1x
= x(xn-k-1 + gn-k-1xn-k-2 + … + g2x + g1 )
= x C’(x) (Cyclic Shifting)
C’(x) has degree less than n-k (Contradiction)
Hence, g0≠0 implies g0=1
The constant term g0 is equal to 1

## Slide 8: Theorem 3
Let g(x) = gn-kxn-k + gn-k-1xn-k-1 +…+ g1x + g0
be the nonzero code polynomial of minimum degree in an (n,k) cyclic code C
Proof:
Assume v(x) is a codeword such that,
v(x) = a(x)g(x)+b(x) (ie not divisible by g(x))
v’(x) = a(x)g(x)
Therefore v(x)=v’(x)+b(x) ie. b(x)=v(x)+v’(x)
This implies b(x) is a valid codeword (Linearity Property)
But degree(b(x))<degree(g(x)) (Contradiction)
A binary polynomial of degree n−1 or less is a code polynomial iff it is a multiple of g(x)

## Slide 9: Theorem 4
Proof:
Every code polynomial v(x) is a multiple of g(x)
v(x) = u(x).g(x)
= (uk-1xk-1 + … + u1x + u0).g(x)
So, an (n,k) cyclic code is completely specified by its non-zero code polynomial of minimum degree g(x), which is the generator polynomial
And the degree of g(x) is equal to the number of parity check digits of the code
In an (n,k) cyclic code, there exists one and only one code polynomial of degree n-k

## Slide 10: Theorem 5
Proof:
xk g(x) is a polynomial of degree n
Dividing xk g(x) by xn + 1, we get,
xk g(x) = (xn + 1) + g(k)(x) (Remainder=g(k)(x))
Right circular shift of g(x) k times gives g(k)(x)
So, g(k)(x) = a(x).g(x) (ie. Multiple of g(x))
This implies, xn + 1 ={xk + a(x)}g(x)
Hence g(x) is a factor of xn + 1
The generator polynomial g(x) of an (n,k) cyclic code, is a factor of xn + 1

## Slide 11: Theorem 6
Proof:
Multiples of g(x) of degree n−1 or less generate a (n,k) linear block code.
If v(x) = vn-1xn-1 + … + v1x + v0
Then x.v(x) = vn-1xn + vn-2xn-1 + … + v1x2 + v0x
= vn-1(xn+1)+(vn-2xn-1 +…+v0x+vn-1)
= vn-1 (xn+1) + v’(x)
So, v’(x) is also a cyclic code polynomial
This implies, the generated code is cyclic
If g(x) is a polynomial of degree n-k & is a factor of xn + 1, then g(x) generates an (n,k) cyclic code

## Slide 12: Generator Matrix
Generator Polynomial
Generator matrix (Non-Systematic Form)
G = gn-k gn-k-1 … g2 g1 g0 0 0 … 0
0 gn-k … g3 g2 g1 g0 0 … 0
...
0 0 … 0 gn-k … g2 g1 g0 k X n
It can be reduced to its systematic form G=[Ik:P] by row transformations
g(x) = gn-kxn-k + gn-k-1xn-k-1 +…+ g1x + g0
Note:

## Slide 13: Parity Check Matrix
For an (n,k) cyclic code
Parity Check Polynomial
Parity Check matrix
H = h0 h1 h2 … hk-1 hk 0 … 0
0 h0 h1 … hk-1 hk 0 … 0
...
0 0 0 … 0 h0 h1 … hk (n-k) X n
h(x) = hkxk + hk-1xk-1 +…+ h2x2 + h1x + h0
xn+1 = g(x) h(x)

## Slide 14: Linear Feedback Shift register
An r-stage shift register
An r-stage linear feedback shift register
An r-stage LFSR with feedback to all stages

## Slide 15: Polynomial Division using LFSR
Let g(x) = x3 + x + 1 = g0 + g1x + g2x2 + g3x3
Then, g0 = 1, g1 = 1, g2 = 0, g3 = 1
and Degree of r(x) < 3
p(x) = x6 + x3 + x + 1=(1001011)2
bout = bf = b2
b2 = b1
b1 = b0 + bf
b0 = bin + bf
r(x) = b2x2 + b1x + b0 = x2 + 1
q(x) = x3 + x
Shift | bin | b0 | b1 | b2 | bf
 |  | 0 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0
2 | 0 | 0 | 1 | 0 | 0
3 | 0 | 0 | 0 | 1 | 0
4 | 1 | 0 | 1 | 0 | 1
5 | 0 | 0 | 0 | 1 | 0
6 | 1 | 0 | 1 | 0 | 1
7 | 1 | 1 | 0 | 1 | 0
Equations:

## Slide 16: Cyclic code Encoding using LFSR(Lower Order)
        For (7,4) cyclic code,
        g(x) = x3 + x + 1
        i(x) = x3 + x
        bout = bf = b2
b2 = b1
b1 = b0 + bf
b0 = bin + bf
d2 = d1
d1 = d0
d0 = bin
ci = ci-1 i≠0
c0 = d2 (Till Shift 7)
c0 = b2 (After Shift 7)
        c(x) = x6 + x4 + x+1
        No. of shifts = 2n-k
Equations:
Shift | bin | b0 | b1 | b2 | bf | d0 | d1 | d2 | c0 | c1 | c2 | c3 | c4 | c5 | c6
 |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
2 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
3 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
4 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
5 |  | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0
6 |  | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0
7 |  | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0
8 |  | 0 | 1 | 1 |  |  |  |  | 0 | 0 | 1 | 0 | 1 | 0 | 0
9 |  | 0 | 0 | 1 |  |  |  |  | 1 | 0 | 0 | 1 | 0 | 1 | 0
10 |  | 0 | 0 | 0 |  |  |  |  | 1 | 1 | 0 | 0 | 1 | 0 | 1

## Slide 17: Cyclic code Encoding using LFSR(Higher Order)
        For (7,4) cyclic code,
        g(x) = x3 + x + 1
        i(x) = x3 + x
        bout = bf = b2+ bin
b2 = b1
b1 = b0 + bf
b0 = bf
ci = ci-1 i≠0
c0 = b2
        c(x) = x6 + x4 + x+1
        No. of shifts = n-k
Equations:
Shift | bin | b0 | b1 | b2 | bf | c0 | c1 | c2 | c3 | c4 | c5 | c6
 |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 1 | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0
2 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
3 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0
4 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0
5 |  | 0 | 1 | 1 |  | 0 | 0 | 1 | 0 | 1 | 0 | 0
6 |  | 0 | 0 | 1 |  | 1 | 0 | 0 | 1 | 0 | 1 | 0
10 |  | 0 | 0 | 0 |  | 1 | 1 | 0 | 0 | 1 | 0 | 1

## Slide 18: Cyclic Code Decoding using LFSR
Recieved codeword = v(x)
Syndrome = s(x) = Rg(x) v(x)
If s(x)==0 then No Error
Else Error
        For (7,4) cyclic code,
          g(x) = x3 + x + 1
          v(x) = x6 + x3 + 1
          s(x) = x2 + x + 1 =(1 1 1)2
If OR (syndrome bits) == 0 then No Error
Else Error
          ie. OR (1 1 1) = 1 or 1 or 1 = 1 implies Error
Detecting condition
Realisation condition
Figure. An Error Detection Decoder

## Slide 19: Cyclic Code Error Correction Process
Received codeword = v(x)
v(x) = c(x) + e(x)
Codeword is always divisible by generator polynomial
Rg(x) c(x) = 0
Syndrome = s(x) = Rg(x) v(x)
s(x) = Rg(x) [c(x) + e(x)]
s(x) = Rg(x) e(x)
Syndrome solely depends on error pattern
Corrected Codeword = c(x) =v(x) + e(x)
Note

## Slide 20: Syndrome Table based Error Detection and Correction
          Considering(7,4) cyclic code,
          g(x) = x3 + x + 1
Figure. An Error-Correction Decoder for (7,4) cyclic code
Syndrome table needs to be stored
in the memory

## Slide 21
          For an (7,4) cyclic code, with g(x) = x3 + x + 1
          Input: v(x) = x6 + x4 + x3 + x + 1
Shift | bin | b0 | b1 | b2 | bf | e0 | e1 | e2 | e3 | e4 | e5 | e6 | d0 | d1 | d2 | d3 | d4 | d5 | d6 | c0 | c1 | c2 | c3 | c4 | c5 | c6
 |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
2 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
3 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
4 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
5 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
6 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
7 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
8 |  |  |  |  |  | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
9 |  |  |  |  |  | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0
10 |  |  |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0
11 |  |  |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0
12 |  |  |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 0
13 |  |  |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0
14 |  |  |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1
Syndrome Table based Error Detection and Correction

## Slide 22: Meggitt Decoder
Avoids the need for a syndrome table (Main Advantage)
Computes error syndromes of all correctable error patterns from a small number of error syndromes
For single error correcting codes all syndromes can be determined from any one error syndrome
For an (n,k) cyclic code with generator polynomial g(x)
e(x) = Error pattern for error at 4th bit from MSB
e’(x) = Error pattern for error at 5th bit from MSB
s(x) = Rg(x) e(x)
s’(x) = Rg(x) e’(x)
Relation between e(x) and e’(x) e’(x) = x . e(x)
Relation between s(x) and s’(x)
s’(x) = Rg(x) [x . e(x)] = Rg(x) [x . s(x)]
s”(x) = Rg(x) [x . S’(x)] = Rg(x) [x2. s(x)]

## Slide 23: Meggitt Decoder with Lower Order Input
          For (7,4) cyclic code, g(x) = x3 + x + 1
          Designing decoder with single-bit error correction capability
          Considering the HIGHEST ERROR PATTERN ie. x6
          Syndrome for x6 is sd(x) = Rg(x) x6 = x2 + 1
          Actual syndrome = s(x) = Rg(x) v(x)
If s(x) = = sd(x)
c0=d6 +1
Else
c0=d6 +0
At SHIFT 7
If s'(x) = = sd(x)
c1=d5+1
Else
c1=d5 +0
At SHIFT 8
At SHIFT 7
...

## Slide 24: Meggitt Decoder with Lower Order Input
          For an (7,4) cyclic code, with g(x) = x3 + x + 1
          Input: v(x) = x6 + x4 + x3 + x + 1
Shift | bin | b0 | b1 | b2 | bf | sd | d0 | d1 | d2 | d3 | d4 | d5 | d6 | c0 | c1 | c2 | c3 | c4 | c5 | c6 | s(x)
 |  | 0 | 0 | 0 | 0 |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0 |  | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
2 | 0 | 0 | 1 | 0 | 0 |  | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | x
3 | 1 | 1 | 0 | 1 | 0 |  | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | x2 + 1
4 | 1 | 0 | 0 | 0 | 1 |  | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
5 | 0 | 0 | 0 | 0 | 0 |  | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
6 | 1 | 1 | 0 | 0 | 0 |  | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
7 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | x + 1
8 |  | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | x2 + x
9 |  | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | x2+x+1
10 |  | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | x2 + 1
11 |  | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 1
12 |  | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | x
13 |  | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | x2
14 |  | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | x + 1

## Slide 25: Meggitt Decoder with Higher Order LFSR
          For (7,4) cyclic code, g(x) = x3 + x + 1
          Considering the HIGHEST ERROR PATTERN ie. x6
          Syndrome for x6 is sd(x) = Rg(x) x6
          Syndrome for x6 for higher order input = s’d(x) = Rg(x) xn-k x6
          = Rg(x) x3 x6 = x2
          Normal error syndrome = s(x) = Rg(x) v(x)
          Error syndrome for higher order input = s’(x) = Rg(x)[xn-k v(x)]
Figure. A Meggitt Decoder with higher order input for (7,4) cyclic code

## Slide 26: Meggitt Decoder with Higher Order LFSR
          For an (7,4) cyclic code, with g(x) = x3 + x + 1
          Input: v(x) = x6 + x4 + x3 + x + 1
Shift | bin | b0 | b1 | b2 | bf | sd | d0 | d1 | d2 | d3 | d4 | d5 | d6 | c0 | c1 | c2 | c3 | c4 | c5 | c6 | s(x)
 |  | 0 | 0 | 0 | 0 |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 1 | 1 | 1 | 0 | 1 |  | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | x + 1
2 | 0 | 0 | 1 | 1 | 0 |  | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | x2 + x
3 | 1 | 0 | 0 | 1 | 0 |  | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | x2
4 | 1 | 0 | 0 | 0 | 0 |  | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
5 | 0 | 0 | 0 | 0 | 0 |  | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
6 | 1 | 1 | 1 | 0 | 1 |  | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | x + 1
7 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | x2 + 1
8 |  | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1
9 |  | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | x
10 |  | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | x2
11 |  | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | x + 1
12 |  | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | x2 + x
13 |  | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | x2 +x+1
14 |  | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | x2 + x